Data Sheet

| Product | Bluetooth Low Energy Module |
| --- | --- |
| Solution | Nordic nRF52810 aQFN Package |
| Model NO. | DK9178D (u.FL Connector) |

Revision History

This table describes the changes to the specification.

| Version | Date | Description |
| --- | --- | --- |
| 1.0.0 | 2024/05/22 | Initial Version |
| 1.0.1 | 2024/05/30 | Add New Label |
| 1.0.2 | 2024/05/31 | Add Marking On Metal Shield |
| 1.0.3 | 2024/05/31 | Packaging Picture Correction |

Index

- Overall Introduction……………………………………………………….………………………………………………..…...5

  - Application………………………………………………………………...............................................5

  - Product Specification……………………………………………………………………………………..…….…5

- Product Dimension…………………………………………………………….…………………………………………….……7

2.1    PCB Dimensions＆Pin Indication………………………………………………………………………….7

2.2    Recommended Layout of Solder Pad………………….…………………………………………..…...8

2.3    RF Layout Suggestion (aka KEEP-Out Area)………………………………………………………..…9

2.4    Pin Assignment……………………………………………………………………………………………….….10

- Main Chip Solution…………………………………………………………………………………………………………….…12

- Shipment Packaging Information………………..………………………………………………………………………..12

  - Tape & Reel Packaging…………………………………….…………………………………………………....13

4.2  Marking on Metal Shield………………………………………………………………………………………..15

- Specification………………………………………………………………………………..…………………………………......16

  - Absolute Maximum Ratings…………………………………………………………………………………..16

  - Operating Conditions…………………………………………………….........................................16

  - Electrical Specifications……………………………………………………………………………………..….17

- Block Diagram……………………………………………………..……………………………………………………………...22

- Antenna……………………………………………………………………………………………………………………………....23

- Reference Circuit…………………………………………………………….………………………………………………..….24

- Notes and Cautions………………………………………………………..…………………………………………………...25

- Basic Facts for nRF52 Family………………………………………..……………………………………………………26

- Useful Links……………………………………………………………………….……………………………………………..27

Full List of Dexatek’s BLE Modules…………………………………………….…………………………………………….…..27

# Overall Introduction

Dexatek’s DK9178D is a BT 5 stack (Bluetooth low energy or BLE) module designed based on Nordic nRF52810 SoC solution, which incorporates: GPIO, SPI, UART, I2C, I2S, PMD, PWM and ADC interfaces for connecting peripherals and sensors

Provides ultra-low power consumption and excellent wireless range with +4 dBm transmission

Power and long range (encoded physical layer) Bluetooth 5 capabilities. New circuits are added

TX power and reduces sleep current for perfect power management.

  - Application

-	Home automation

-	Building automation

-	Industrial

-	Health/fitness sensor and monitor devices

-	Key fobs and wrist watches

-	Remote controls

-	Gaming controllers

-	Remote control toys

-	Mouse

-	Keyboard

-	Gaming

1.2 Product Specification

Feature

- Bluetooth ® 5 2.4 GHz transceiver,

- LE 2M PHY, LE 1M PHY

- 1 Mbps, 2 Mbps Bluetooth® low energy mode

- Proprietary 2.4 GHz – 2 Mbps, 1 Mbps

- nRF52810, ARM ® Cortex ® M4 32-bit processor with FPU, 64 MHz

- 192kB Flash and 24kB RAM

- Radio

- GFSK at 1 Mbps and 2 Mbps,

- -96 dBm sensitivity in Bluetooth ® low energy mode

- -20 to +4 dBm TX power, configurable in 4 dB steps

- Power Management

  - 1.7 V to 3.6 V supply voltage range

- Security features

  - AES HW encryption with EasyDMA

- Peripheral interface / Hardware

  - Programmable peripheral interconnect (PPI)

  - 32 general purpose I/O pins (GPIO)

  - Nordic SoftDevice ready with support for concurrent multiprotocol

  - 12-bit, 200 ksps ADC – 8 configurable channels with programmable gain

  - 64 level comparator

  - 4-channel pulse width modulator (PWM) unit with EasyDMA

  - digital microphone interface (PDM)

  - 3x 32-bit timer with counter mode

  - SPI master/slave with EasyDMA

  - Up to 2x I2 C compatible two-wire master/slave

  - UART (CTS/RTS) with EasyDMA

  - Quadrature decoder (QDEC)

  - 2x real-time counter (RTC)

- Operation Temperature: -40 °C to 85 °C

# Product Dimension

2.1.	PCB Dimensions & Pin Indication

2.2.	Recommended Layout of Solder Pad

2.3.	RF Layout Suggestion (aka Keep-Out Area)

Please follow below instruction to avoid from having Ground Pad in the area of our RF test pad. Otherwise, it may cause shortage to the module

2.4.	Pin Assignment

3. Main Chip Solution

| RF IC | Crystal Frequency |
| --- | --- |
| Nordic NRF52810 | 32MHZ |

32MHz crystal and RF (VDD) DC/DC inductor (Reg1) are already inside the module.

4.	Shipment Packaging Information

| Model | Antenna | Photo |
| --- | --- | --- |
| DK9178D | u.FL Connector |  |

※Unit Weight of Module: 0.68g (±0.02g)

※Packaging Type: Anti-static Tape & Ree

|  | Tape & Reel |
| --- | --- |
| MPQ (Min. Package Qty) | 600 pcs per reel |
| Carton Contents (per Carton) | 600 pcs |
| Carton Dimension L*W*H cm | 37*36*6 |
| Gross Weight | About 1.9kgs |

4.1 Tape & Reel Packaging

| Part Number | DK91xxD |
| --- | --- |
| Quantity | 600 pcs |
| Date Code | 24xx |

4.2. Marking on Metal Shield

4.2.1. Label

5. Specification

Any technical spec shall refer to Nordic’s official documents as final reference.

5.1. Absolute Maximum Ratings

5.2. Operating Conditions

5.3. Electrical Specifications

5.3.1. General Radio Characteristics

5.3.2. Radio Current Consumption (Transmitter)

5.3.3. Radio Current Consumption (Receiver)

5.3.4. Transmitter Specification

5.3.5. RSSI Specification

5.3.6. Receiver Operation

5.3.7. RX Selectivity

5.3.8. RX Intermodulation

5.3.9. Radio Timing

5.3.10. CPU

5.3.11. Power Management

6. Block Diagram

7. Antenna

Below chart shows a few options of external antenna which has been tested and approved to use with DK9178D

| # | Photo | Model No. | Type | Supplier | Gain | Certification |
| --- | --- | --- | --- | --- | --- | --- |
| 1 |  | ANTX100 ETHAB24553 | External | Yageo | ≦ 2 dBi | FCC, IC, NCC, CE |
| 2 |  | ANTX100 P011B24003 | PCB | Yageo | ≦2.2 dBi | FCC, IC, NCC, CE |
| 3 |  | ANTX100 P111B24003 | PCB | Yageo | ≦3.3 dBi | FCC, IC, NCC, CE |

8. Reference Circuit

This is a notification for circuit combinations and please refer below caution for specification, and carefully in detail description as applies to adapt on peripherals circuits.

The module default is define on “LDO mode” and must add external 32.768 kHz crystal for MCU boot up.

Pin DEC4 had built in 1𝛍𝐅 decoupling capacitor in module.

Please remove Y1/C7/C9 when using the internal 32MHz RC oscillator.

Please add L1/L2/C2 in circuit if power setup “DC-DC” mode.

9. Notes and Cautions

1. Follow the conditions written in this specification, especially the control signals of this module.

2. The supply voltage should abide by the maximum ratings and must to supply within range of specification.

4. This module should not be mechanically stressed when installed.

5. Keep this module away from heat. Heat is the major cause of decreasing the life time of these modules.

6. Avoid assembly and use of the target equipment in conditions where the module temperature may exceed the maximum tolerance.

7. Keep this module away from other high frequency circuits.

8. Refer to the recommended pattern when designing a board.

9. Do not expose modules under direct sunlight for long duration. Modules should be kept away from humid and salty air conditions, and any corrosive gasses or substances. Store it within -40℃ to +125℃ before and after installation.

10. Basic Facts for nRF52 Family

Below chart shows basic spec for Nordic nRF52 family, which is helpful to understand the differences between each SoC. Any discrepancy shall referto Nordic’s technical document as final reference.

| Solution | Nordic 52840 | Nordic 52833 | Nordic 52832 | Nordic 52810 |
| --- | --- | --- | --- | --- |
| Antenna | Ipex | Ipex |
| Antenna Vendor | Χ | Χ |
| RAM (KB) | 256KB | 128KB | 64KB | 24KB |
| Internal Flash | 1MB | 512KB | 512KB | 192KB |
| External flash | Χ | Χ | Χ | Χ |
| PIN OUT | 48 | 42 | 32 | 32 |
| Shielding Case | O | O | O | O |
| Package | 6x6mm QFN48 | 7x7mm aQFN™73 | 6x6mm QFN48 | 6x6mm QFN48 |
| RF | BT5.3 | BT5.3 | BT5.3 | BT5.3 |
| PA | Χ | Χ | Χ | Χ |
| Operating Temp | -40~85C | -40~105C | -40~85C | -40~85C |
| Tx Power(MAX) | 8dBm | 8dBm | 4dBm | 4dBm |
| Supply Voltage | 1.7V~5.5V | 1.7V~5.5V | 1.7V~3.6V | 1.7V~3.6V |

11. Useful Links

- Nordic Infocenter: Nordic Semiconductor Infocenter

- Nordic DevZone: Nordic Devzone Q&A

- Nordic Document: Nordic Techdoc

- Nordic Academy : Nordic DevAcademy

- nRF52810 Product Specification: nRF52810 - Bluetooth 5.2 SoC - nordicsemi.com

Full List of DEXATEK’s BLE Modules

| Nordic Solution | DEXATEK NO. | Antenna | RAM | Flash Memory |
| --- | --- | --- | --- | --- |
| nRF52840 | DK9177A | IPEX | 256 kB | 1 MB |
| nRF52832 | DK9178C | IPEX | 64 kB | 512 kB |
| nRF52832 | DK9180C | PCB | 64 kB | 512 kB |
| nRF52840 | DK9181A | PCB | 256 kB | 1 MB |
| nRF52832 | DK9182C | CHIP | 64 kB | 512 kB |
| nRF52840 | DK9183A | CHIP | 256 kB | 1 MB |
| nRF52833 | DK9177B | IPEX | 128 kB | 512 kB |
| nRF52810 | DK9178D | IPEX | 24 kB | 192 kB |
| nRF52810 | DK9180D | PCB | 24 kB | 192 kB |
| nRF52833 | DK9181B | PCB | 128 kB | 512 kB |
| nRF52810 | DK9182D | CHIP | 24 kB | 192 kB |
| nRF52833 | DK9183B | CHIP | 128 kB | 512 kB |